## Slide 1: On the Effectiveness of OpenMP teams for Programming Embedded Manycore Accelerators
Andrea Marongiu
Swiss Federal Institute of
Technology in Zurich (ETHZ)
a.marongiu@iis.ee.ethz.ch
Work supported by
FP7 – ICT
GRANT N° 611016
Alessandro Capotondi
University of Bologna

## Slide 2: Outline
Motivation
  Heterogeneous architectures
  Manycore accelerators
NUMA communication and OpenMP
  Flat parallelism
  Nested parallel regions
  OpenMP teams and the distribute directive
  Other constructs for non-loop parallelism
Experimental setup and results

## Slide 3: Heterogenous Manycores
Ever-increasing demand for computational power has recently led to radical evolution of computer architectures
Two design paradigms have proven effective in increasing performance and energy efficiency of compute systems
  >Many-cores
  >Architectural Heterogeneity
A common template is one where a powerful general-purpose processor (the host) is coupled to one or more a many-core accelerators
Notes: Add some pictures such as k1 kalray +add virtualization and embedded hpc

## Slide 4: Heterogenous Manycores
True virtually in every computing domain and at every scale!
Shoubu RIKEN
Xeon E5-2618Lv3
8C 2.3GHz
Infiniband FDR
PEZY-SC
Kalray MPPA256
NVIDIA Tegra X1
Titan Cray X47
Opteron 6274
16C 2.2GHz
Cray Gemini
NVIDIA K20x
Tianhe-2
Xeon E5-2692
12C 2.2GHz
TH Express-2
Intel Xeon Phi
TI KeystoneII
SERVER / SUPERCOMP
SoC
Notes: Add some pictures such as k1 kalray +add virtualization and embedded hpc

## Slide 5: HETEROGENEOUS MANYCORES
Manycore accelerators share many commonalities across computing domains..
  Cluster-based design  NUMA
  Explicitly managed memories

## Slide 6: PEZY-SC 1024
Dominates the Green500
Heavily cluster-based
http://www.pezy.co.jp/en/products/pezy-sc.html
http://news.mynavi.jp/articles/2014/09/17/pezy/
Logic Cores(PE) | 1,024
Core Frequency | 733MHz
Peak Performance | Floating Point Single 3.0TFlops / Double 1.5TFlops
Host Interface | PCI Express GEN3.0 x8Lane x 4Port (x16 bifurcation available) JESD204B Protocol support
DRAM Interface | DDR4, DDR3 combo 64bit x 8Port Max B/W 1533.6GB/s +Ultra WIDE IO SDRAM (2,048bit) x 2Port Max B/W 102.4GB/s
Control CPU | ARM926 2core
Process Node | 28nm
Package | FCBGA 47.5mm x 47.5mm, Ball Pitch 1mm, 2,112pin

## Slide 7: NVIDIA K20
15 clusters (SMX) sharing L2 SPM
192 cores per SME, sharing 64KB L1 SPM
1.17 DP TFLOPS - 3.52 SP TFLOPS
235 W

## Slide 8: Kalray MPPA 256
16 clusters
16 cores per cluster, sharing 2MB L1 SPM/cache
1.25 TFLOPS
25 GOPS/W – 75 GOPS/W
Image, audio, signal processing
Control commands (aeronautics, industrial automation)

## Slide 9: STHORM
NoC
L2 SPM
AXI BRIDGE
4 clusters
16 cores per cluster, sharing 256KB L1 data SPM
80 GOPS @ 2W
Notes: Questa piattaforma, non nasce con il solo scopo di essere standalone. Perché manca il parallelismo, manca anche la potenza «computazione» nel singolo core.
Il controllo nell’host, acceleratore per le parte computazionali intense

## Slide 10: NUMA communication
CL
NI
R
CL
NI
R
CL
NI
R
CL
NI
R
PE
#0
PE
#1
PE
#15
TCDM
CLUSTER 1
. . .
Network Interface
I$
I$
I$
data
PE
#0
PE
#1
PE
#15
TCDM
CLUSTER 2
. . .
Network Interface
I$
I$
I$
data2
PE0 on CLUSTER 1 writes on data
Local communication
1 cycle latency
PE0 on CLUSTER 0 writes on data2
Remote communication
Increasing latency with distance

## Slide 11: CrowdED constellation of Programming models
Proprietary
Programming models
Khronos Standard for
Heterogeneous Computing
Standard
for shared memory system
Academic
Proposals
OmpSS
OpenHMPP
…

## Slide 12: OpenMP
De-facto standard for shared memory programming
Support for nested (multi-level) parallelism  good for clusters
Annotations to incrementally convey parallelism to the compiler  increased ease of use
Based on well-understood programming practices (shared memory, C language)  increases productivity
“OpenCL for programming shared memory multicore CPUs” by Akhtar Ali , Usman Dastgeer , Christoph Kessler

## Slide 13: OpenMP
De-facto standard for shared memory programming
Support for nested (multi-level) parallelism  good for clusters
Annotations to incrementally convey parallelism to the compiler  increased ease of use
Based on well-understood programming practices (shared memory, C language)  increases productivity
Designed for uniform SMP with main shared memory
Lacks constructs to control accelerators
  And compilation toolchain to deal with multiple ISA..
  ..and multiple runtime systems too!!
But…
Intel’s Parallel Universe magazine – May 2014
?
Notes: Virtical starts in 2011 to target this issue

## Slide 14: FORK-JOIN PARALLELISM
OpenMP leverages a fork-join execution model
The program starts on a single thread (the master), then new threads are recruited upon entering a parallel region
Parallelism in application is always found at multiple levels, in a hierarchical manner
  How to capture this in the program?
  How to map the wokload in a NUMA-aware manner?

## Slide 15: NESTED PARALLELISM
while(1)
{
#pragma omp parallel num_threads(4)
{
#pragma sections
{
#pragma section
{
#pragma omp parallel num_threads(16)
ColorScaleConv();
}
#pragma section
{
#pragma omp parallel num_threads(16)
cvThreshold();
}
#pragma section
{
#pragma omp parallel num_threads(16)
cvMoments();
}
#pragma section
{
#pragma omp parallel num_threads(16)
cvAdd();
}
}
}
}
A.
C
E
G
A
E
E
B
E
F
D
E
H
C
E
G
A
E
E
B
E
F
D
E
H
B.
C.
D.
void ColorScaleConv()
{
for(i = 0; i < FRAME_SIZE; i++)
{
[ALGORITH]
}
}
#pragma omp for
A powerful abstraction for specifying structured parallelism
And very suitable for NUMA (cluster-based) systems
But what about PHYSICAL thread mapping?

## Slide 16: Nested Parallelism CLUSTER-AWARE
while(1)
{
#pragma omp parallel
{
#pragma sections
{
#pragma section
{
#pragma omp parallel
ColorScaleConv();
}
#pragma section
{
#pragma omp parallel
cvThreshold();
}
#pragma section
{
#pragma omp parallel
cvMoments();
}
#pragma section
{
#pragma omp parallel)
cvAdd();
}
}
}
}
A.
C
E
G
A
E
E
B
E
F
D
E
H
C
E
G
A
E
E
B
E
F
D
E
H
CL
NI
R
CL
NI
R
CL
NI
R
CL
NI
R
PE
#0
PE
#1
PE
#15
TCDM
CLUSTER i
. . .
Network Interface
I$
I$
I$
data[i]
E
E
C
E
G
A
E
E
B
E
F
D
E
H
B.
C.
D.
void ColorScaleConv()
{
for(i = 0; i < FRAME_SIZE; i++)
{
[ALGORITH]
}
}
#pragma omp for

## Slide 17: NUMA-unaware Thread mapping
Cluster 0
PE0
PE1
Cluster 1
PE2
PE3
PE0
PE1
PE2
PE3
Cluster 2
PE0
PE1
PE2
PE3
Cluster 3
PE0
PE1
PE2
PE3
T0
T1
T0
T0
T1
T0

## Slide 18: NUMA-unaware Thread mapping
Cluster 0
PE0
PE1
Cluster 1
PE2
PE3
PE0
PE1
PE2
PE3
Cluster 2
PE0
PE1
PE2
PE3
Cluster 3
PE0
PE1
PE2
PE3
T1
T1
T1
T0
T0
T0
T0
T1
T0
T1
T0
T1
T0

## Slide 19: NUMA-unaware Thread mapping
Cluster 0
PE0
PE1
Cluster 1
PE2
PE3
PE0
PE1
PE2
PE3
Cluster 2
PE0
PE1
PE2
PE3
Cluster 3
PE0
PE1
PE2
PE3
T1
T1
T0
T0
T0
T0
T0
T0
T1
T2
T3
T1
T2
T3
T1
T2
T3
T1
T2
T3
T0
T0
T1
T0
T1
T0
T1
T0
T1
T2
T3
T0
T1
T2
T3
T0
T1
T2
T3
T0
T1
T2
T3

## Slide 20: LOCALITY-AWARE WORKLOAD DISTRIBUTION
How to best distribute parallel workload within a cluster-based manycore accelerator?
  Flat parallelism?
  Nested parallel for?
  The distribute directive: Teams and leagues
  And how about non-loop centric parallelism?

## Slide 21
#pragma omp target map(in, out)
{
for(stripe = 0;
stripe < N_STRIPES;
++stripe)
{
dma_in(in[stripe]);
KER (in[stripe], out[stripe]);
dma_out(out[stripe]);
}
}
void KER(in1, in2, out) {
#pragma omp parallel for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
R
R
R
R
flat parallel thread team
PE 0
L1
BUF0
PE 1
PE 2
PE 3
PE 4
PE 5
PE 6
PE 7
PE 16
L1
PE 17
PE 18
PE 19
PE 20
PE 21
PE 22
PE 23
PE 24
L1
PE 25
PE 26
PE 27
PE 28
PE 29
PE 30
PE 31
PE 8
L1
PE 9
PE 10
PE 11
PE 12
PE 13
PE 14
PE 15
master thread
slave thread
outer team
inner team
The role of DMA in explicitly managed memory hierarchies!

## Slide 22: LOCALITY-AWARE WORKLOAD DISTRIBUTION
How to best distribute parallel workload within a cluster-based manycore accelerator?
  Flat parallelism?
  Nested parallel for?
  The distribute directive: Teams and leagues
  And how about non-loop centric parallelism?

## Slide 23
#pragma omp target map (in, out)
#pragma omp parallel num_threads(4)
for(stripe = 0;
stripe < N_STRIPES;
++stripe)
{
dma_in(in[stripe]);
KER (in[stripe], out[stripe]);
dma_out(out[stripe]);
}
}
R
R
R
R
PE 0
L1
B0
PE 1
PE 2
PE 3
PE 4
PE 5
PE 6
PE 7
PE 16
L1
PE 17
PE 18
PE 19
PE 20
PE 21
PE 22
PE 23
PE 24
L1
PE 25
PE 26
PE 27
PE 28
PE 29
PE 30
PE 31
PE 8
L1
PE 9
PE 10
PE 11
PE 12
PE 13
PE 14
PE 15
master thread
slave thread
outer team
inner team
void KER(in1, out) {
#pragma omp parallel for \
num_threads(16)
for(i = 0; i < … ; i++)
[ALGORITHM]
}
nested team
B1
B2
B3

## Slide 24: LOCALITY-AWARE WORKLOAD DISTRIBUTION
How to best distribute parallel workload within a cluster-based manycore accelerator?
  Flat parallelism?
  Nested parallel for?
  The distribute directive: Teams and leagues
  And how about non-loop centric parallelism?

## Slide 25
#pragma omp target teams num_teams(4) map (in, out)
#pragma omp distribute
for(stripe = 0;
stripe < N_STRIPES;
++stripe)
{
dma_in(in[stripe]);
cvADD (in[stripe], out[stripe]);
dma_out(out[stripe]);
}
}
R
R
R
R
PE 0
L1
B0
PE 1
PE 2
PE 3
PE 4
PE 5
PE 6
PE 7
PE 16
L1
PE 17
PE 18
PE 19
PE 20
PE 21
PE 22
PE 23
PE 24
L1
PE 25
PE 26
PE 27
PE 28
PE 29
PE 30
PE 31
PE 8
L1
PE 9
PE 10
PE 11
PE 12
PE 13
PE 14
PE 15
master thread
slave thread
outer team
inner team
B1
B2
B3
void KER(in1, out) {
#pragma omp parallel for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
distributed nested team

## Slide 26: LOCALITY-AWARE WORKLOAD DISTRIBUTION
How to best distribute parallel workload within a cluster-based manycore accelerator?
  Flat parallelism?
  Nested parallel for?
  The distribute directive: Teams and leagues
  And how about non-loop centric parallelism?

## Slide 27: NON-loop CONSTRUCTS?
NEW! Clause on specification v4.0 coupled to the parallel directive to specify thread mapping:
master: assigns every thread to the same place as the master thread.
close: assigns threads to places close to the place of the parent’s
Thread.
spread: creates a sparse distribution for a team of T threads among the P places of the parent’s place partition.
For NUMA

## Slide 28: Nested Parallelism CLUSTER-AWARE
while(1)
{
#pragma omp parallel
{
#pragma sections
{
#pragma section
{
#pragma omp parallel
ColorScaleConv();
}
#pragma section
{
#pragma omp parallel
cvThreshold();
}
#pragma section
{
#pragma omp parallel
cvMoments();
}
#pragma section
{
#pragma omp parallel)
cvAdd();
}
}
}
}
A.
C
E
G
A
E
E
B
E
F
D
E
H
C
E
G
A
E
E
B
E
F
D
E
H
CL
NI
R
CL
NI
R
CL
NI
R
CL
NI
R
PE
#0
PE
#1
PE
#15
TCDM
CLUSTER i
. . .
Network Interface
I$
I$
I$
data[i]
E
E
C
E
G
A
E
E
B
E
F
D
E
H
B.
C.
D.
void ColorScaleConv()
{
for(i = 0; i < FRAME_SIZE; i++)
{
[ALGORITH]
}
}
#pragma omp for
proc_bind (spread)
proc_bind (close)
proc_bind (close)
proc_bind (close)
proc_bind (close)

## Slide 29: Experimental Setup
ZYNQ
FPGA
S
M
SM2
SS1
PS1
PM1
STHORM SoC
2D port2
2D port1
2D GPIOs
29
RAB
RAB
SNoC2AXI
AXI2SNoC
16-bit
2D SNoC
47
64-bit
2D SNoC
113
PIO1
SIO0
Ref. clock, Sys. Clock, Reset, JTAG, Trace, interrupts…
GPIO
DRAM
IO periph
ARM A9
ARM A9
L1
L1
snoop
L2
DRAM ctrl
AXI interconnect
L2 ctrl
GIC
IO periph
STHORM BOARD
Notes: Anche il system on board permette lo shared memory attraverso il bridge. Questo sistema permette di accedere attraverso la DRAM.
Bandwith limitato.
RAB (Remap Address Block)

## Slide 30: Experimental Setup
We consider 6 benchmarks from the image processing/computer vision domain
Acronym | Brief explanation
STRAS | Matrix multiplication using Strassen decomposition
GSID | Generalized squared interpoint distance
LRFR | Local reference frame radius (surface matching)
HIST | Histogram interpolation
NCC | Normalized cross-correlation algorithm
CT | Object tracking based on a specific color
FAST | Corner detector

## Slide 31: Experimental Setup (2)
FAST is highly sensitive to input data
  Image size
  Image composition (number of corners)
Acronym | Brief explanation
1.5%_S | 1.5% corner density in a small image (QVGA)
6%_S | 6% corner density in a small image
15%_S | 15% corner density in a small image
1.5%_L | 1.5% corner density in a large image (VGA)
6%_L | 6% corner density in a large image
15%_L | 15% corner density in a large image

## Slide 32: NUMA-aware Nested Parallelism
5x avg speedup wrt flat parallelism
Chart: SPEEDUP
| 1.5%_S | 6%_S | 15%_S | 1.5%_L | 6%_L | 15%_L | STRAS | GSID | LRFR | HIST | NCC | CT | FAST |  | AVG
parallel for | 15.2 | 14.96 | 15.0251 | 8.0241 | 12.02 | 0.77161 | 6.892 | 7.2997 | 7.8271 | 10.1007 | 9.6698 | 15.629 | 9.7991
nested parallel for | 1.02 | 1.01 | 1.0174 | 0.89245 | 0.96 | 0.82658 | 0.92495 | 0.87622 | 0.9894 | 1.0103 | 0.97922 | 1.0376 | 0.95514
distribute | 47.26 | 60.8286 | 59.265 | 41.6121 | 61.48 | 19.5551 | 22.6675 | 30.9908 | 28.9169 | 45.7576 | 49.2593 | 60.1971 | 42.5084
Notes: Submitted Elsevier Parallel computing

## Slide 33
#pragma omp target teams num_teams(4)
#pragma omp distribute
for(stripe = 0;
stripe < N_STRIPES;
++stripe)
{
dma_in(in[stripe]);
CSC (in[stripe], tmp1[stripe]);
cvTHR (tmp1[stripe], tmp2[stripe]);
cvMOM (tmp2[stripe], xy[stripe]);
}
#pragma omp barrier
#pragma omp distribute
for(stripe = 0;
stripe < N_STRIPES;
++stripe)
{
dma_in(in[stripe]);
dma_in(track[stripe]);
cvADD (in[stripe], track[stripe], out[stripe]);
dma_out(out[stripe]);
}
}
void CSC(in, tmp1) {
#pragma omp for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
void cvTHR(tmp1, tmp2) {
#pragma omp for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
void cvMOM(tmp2, xy) {
#pragma omp for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
void cvADD(in1, in2, out) {
#pragma omp parallel for
for(i = 0; i < … ; i++){
[ALGORITHM]
}
}
distributed nested team
Chart: 
| teams region 1 | teams region 2 | overall
SPEEDUP | 48.33 | 7.26 | 19.56
CT

## Slide 34: On the Effectiveness of OpenMP teams for Programming Embedded Manycore Accelerators
Andrea Marongiu
Swiss Federal Institute of
Technology in Zurich (ETHZ)
a.marongiu@iis.ee.ethz.ch
Work supported by
FP7 – ICT
GRANT N° 611016
Alessandro Capotondi
University of Bologna